## Slide 1
Anti-Spam Filtering
over Delay-Tolerant Networks
Measuring how anti-spam tools behave on an Earth–Moon link
Rakesh Lakshmanan · MSc Dissertation · Trinity College Dublin
1.3 s
page 1/9
Notes: Good morning. My project is about anti-spam filtering over delay-tolerant networks. The question I set out to answer is a simple one: do the anti-spam tools a mail server runs today still work when that mail server is on the Moon, and the services it depends on are on Earth.

## Slide 2
Delay-Tolerant Networking
Why standard internet protocols do not work in space
No continuous end-to-end path
Delay in seconds, not milliseconds
Protocol timeouts and handshakes assume short round trips
DTN uses store-and-forward
Earth
Relay
Moon
Each node stores the message and forwards it when a link is available.
Specified in RFC 4838 and RFC 9171. NASA's ION is one implementation of the Bundle Protocol.
Email is already carried this way
Mail server
on Earth
Gateway packs
a bundle
Bundle crosses
the link
Gateway
rebuilds it
Mail server
on the Moon
Email transport over DTN is specified and implemented.
page 2/9
Notes: First, why we need a special network for this at all. Standard internet protocols do not work in space, for two reasons. There is no continuous end-to-end path, and the delay is in seconds, not milliseconds. Protocol timeouts and handshakes assume short round trips, and in space that assumption does not hold.
The answer is delay-tolerant networking, which uses store-and-forward. Each node stores the message and forwards it when a link is available. It is not experimental: it is specified in RFC 4838 and RFC 9171, and NASA's ION is one implementation of the Bundle Protocol.
Email is already carried this way. A standard mail server on Earth, a gateway that packs the message into a bundle, the bundle crosses the link, a gateway rebuilds it, and a standard mail server on the Moon receives it. Email transport over DTN is specified and implemented.

## Slide 3
The Problem
Email transport over DTN has been studied.
Filtering has not.
Anti-spam tools do not only read the message. Each check is a network lookup: DNS blocklists, sender reputation, shared spam databases.
On the Moon node, each lookup takes 2.6 s.
The effect on filtering has not been measured.
One scan on the Moon node
Read the message
instant
Check the sender IP
2.6 s
Check each URL
2.6 s
Follow-up lookups
2.6 s
Produce a verdict
—
page 3/9
Notes: So email transport over DTN has been studied. Filtering has not. That gap is the problem.
The reason it matters is on the right. Anti-spam tools do not only read the message. Reading the message is instant. But every other step is a network lookup: check the sender IP, check each URL, follow-up lookups. On Earth these are fast. On the Moon node, each lookup takes 2.6 seconds. Reading is free; the lookups are not.
So a mail service on the Moon receives spam like any mail system, and the tools that would catch it depend on lookups that cross the delayed link. The effect on filtering has not been measured. That is what I measure.

## Slide 4
Research Question
How do existing anti-spam tools behave over a delay-tolerant link,
and what mechanisms drive that behaviour?
Network dependence
How does each tool's network dependence interact with delay?
Failure modes
What fails under delay, and what causes it?
Timeouts
How do the tools' own timeout settings behave under delay?
Scope
A behavioural study. It characterises and explains the response to delay. It does not propose a filtering system for interplanetary email.
page 4/9
Notes: The research question is: how do existing anti-spam tools behave over a delay-tolerant link, and what mechanisms drive that behaviour.
It has three parts. Network dependence: how does each tool's network dependence interact with delay. Failure modes: what fails under delay, and what causes it. And timeouts: how do the tools' own timeout settings behave under delay.
On scope: this is a behavioural study. It characterises and explains the response to delay. It does not propose a filtering system for interplanetary email. The output is an account of the behaviour and its causes, which is the starting point for anyone who later builds filtering into interplanetary email.

## Slide 5
Testbed
Earth — 192.168.100.0/24
Moon — 192.168.200.0/24
Mail1Client
Thunderbird
user
Mail1
192.168.100.10
Postfix, Dovecot
Mail2
192.168.200.11
anti-spam scan
Mail2Client
Thunderbird
user
Space
192.168.100.1 / .200.1
relay
applies the delay
IMAP / SMTP
IMAP / SMTP
no delay
1.3 s each way
Blocklists
(on Earth)
each lookup from the scanner: 2.6 s round trip
The blocklists are on Earth. Queries from Earth are not delayed. Queries from the Moon cross the link twice.
Every component is production mail software (Postfix, Dovecot, SpamAssassin, rspamd), not simulated. Only the link delay is introduced.
page 5/9
Notes: This is the testbed. Two networks: Earth and Moon. On Earth, a Thunderbird client and the sending mail server, Mail1, running Postfix and Dovecot. On the Moon, the receiving mail server, Mail2, which runs the anti-spam scan, and its own Thunderbird client. Between them sits the relay, called Space, and that is where the delay is applied: no delay on the Earth side, 1.3 seconds each way across the link.
The key point is the asymmetry. The blocklists are on Earth. Queries from Earth are not delayed. But queries from the Moon cross the link twice, so each lookup from the scanner is a 2.6-second round trip. The scanner is on the far side of the delay, and that is what the experiment measures.
One thing I want to stress: every component is production mail software. Postfix, Dovecot, SpamAssassin, rspamd. Nothing is simulated. Only the link delay is introduced.

## Slide 6
Software
Mail
Postfix
mail transfer agent
Dovecot
IMAP / POP3 server
Thunderbird
mail client
DTN
ION-DTN 4.1.4
Bundle Protocol implementation
BPMail
carries email over the Bundle Protocol
Anti-spam
SpamAssassin
DNS blocklists
Rspamd
DNS, many parallel lookups
Vipul's Razor
TCP to a central server
The anti-spam tools are the object of study. The rest provides the mail path they run on.
The three tools were selected for their different network dependencies: DNS blocklists, a large volume of parallel DNS lookups, and a TCP session to a central server.
page 6/9
Notes: Here is the software, in three columns. The mail column is standard, unmodified mail software: Postfix as the mail transfer agent, Dovecot for IMAP and POP3, Thunderbird as the client. The DTN column carries the message over the Bundle Protocol: ION-DTN and BPMail.
The right-hand column is the object of study, the anti-spam tools. The rest just provides the mail path they run on. I selected three tools for their different network dependencies. SpamAssassin uses DNS blocklists. Rspamd also uses DNS, but issues a large volume of parallel lookups. Vipul's Razor opens a TCP session to a central server. Three tools, three different ways of reaching the network, so each may behave differently under delay.

## Slide 7
Run Protocol
Run 1
No delay
Baseline
Run 2
1.3 s delay
Default settings
Run 3
1.3 s delay
Reduced timeout
681
emails, the same corpus each run
Per email
verdict, score, rules fired, scan time
Per run
packet capture, cold DNS cache
page 7/9
Each run is scripted end to end: the sender streams the corpus, the scanner records the results below. A full pass repeats identically with no per-email steps.
Notes: The run protocol is three runs per tool. Run 1 is the baseline, with no delay. Run 2 applies the 1.3-second delay with the tool's default settings. Run 3 keeps the delay but reduces the timeout, which is what an operator might do to keep mail moving.
Each run uses the same 681 emails, the same corpus every time. For each email I record the verdict, the score, the rules fired, and the scan time. For each run I take a packet capture and start from a cold DNS cache. Each run is scripted end to end, so a full pass repeats identically with no per-email steps. Runs 2 and 3 are run back-to-back, because blocklist listings drift over hours, so only adjacent runs can be compared fairly.

## Slide 8
Results — Rspamd
Chart: 
| No delay | Delay | Delay + reduced timeout
Flagged as spam | 675 | 654 | 569
Real blocklist hit | 502 | 482 | 94
681 emails, three runs
Delay, default settings
Detection drops 99.1% to 96.0%. Lookups still complete.
Scan time rises 12×
0.47 s to 5.61 s mean. DNS queries 39k to 81k.
Reduced timeout
Blocklist hits 502 to 94. 103 emails flip to not-spam.
Packet captures show the resolver returned every answer. The loss is caused by the tool's timeout, not by network failure.
page 8/9
Notes: Now the results. I want to be clear up front: only one of the tools' results is displayed here. These are the rspamd results. The full set for all tools is in the dissertation.
Start with delay on default settings, the middle case. Detection drops from 99.1 percent to 96.0 percent. That is a drop of three points. It is small, and the reason it is small is important: the lookups still complete. The answers arrive across the delayed link, and the tool waits for them.
The cost of waiting shows up in scan time. Scan time rises twelve times: from 0.47 seconds to 5.61 seconds on average. And DNS queries go from 39,000 to 81,000, roughly double, because queries are retransmitted while the tool waits. So under default settings, rspamd keeps almost all of its detection, but it pays for it in time.
Now the reduced timeout, Run 3. Here detection falls sharply. Real blocklist hits drop from 502 to 94. And 103 emails that were spam in Run 2 flip to not-spam in Run 3.
The key finding is why. The packet captures show the resolver returned every answer, in all cases. The loss is caused by the tool's timeout, not by network failure. When the timeout is 1.5 seconds and the round trip is 2.6 seconds, the tool ends the task before the answer arrives. The network delivered; the tool gave up early.
(If asked about the crash: rspamd would not scan any email containing a URL until I worked around a CPU-feature misreport in the virtualisation layer. Diagnosed from a core dump, confirmed against upstream bug reports. It is not a DTN effect.)

## Slide 9
Summary
The testbed runs: the scanner is on the Moon node, and the delay is applied to the Moon link only.
The delay does not prevent the lookups completing. The tool's timeout does.
Detection that survives a reduced timeout comes from the resolver cache, not from completed lookups.
Under delay, Rspamd retained detection at 12× the scan time. With the timeout reduced, most DNS-based detection was lost.
page 9/9
Two tasks remain: the Razor run analysis is being completed, and the dissertation write-up is in progress.
Notes: To summarise. The testbed runs, and the design choice that matters is validated: the scanner sits on the Moon node, and the delay is applied to the Moon link only.
The main result is one line. The delay does not prevent the lookups completing. The tool's timeout does. Under delay, rspamd retained detection at twelve times the scan time. With the timeout reduced, most DNS-based detection was lost. And the detection that does survive a reduced timeout comes from the resolver cache, from answers already held from earlier messages, not from completed lookups.
Two tasks remain. The Razor run analysis is being completed, and the dissertation write-up is in progress.